## Slide 1: Multi-Loop Control Decoupler Design

## Slide 2: Niederlinsky Index
Consider MIMO system whose inputs and outputs are paired as i.e, Transfer Function matrix G(s) is arranged such that transfer functions relating paired inputs and outputs are arranged along the diagonal.
Further, let each element of G(s) be (a) rational and (b) open loop stable.
Also, let n SISO feedback controllers with integral action be designed such that each SISO loop is stable when all the rest ( n-1) loops are open.
Under these assumptions, the multi-loop control system will be unstable for all possible values of controller parameters if the Niederlinsky Index (NI) defined as

## Slide 3: Furnace Control

## Slide 4: Multi-Loop PID Control
After selection of loop pairings with minimum interactions, one can design controllers for individual loops.
Presence of interaction and retaliatory effects from other loops may require that the controller be detuned for acceptable performance.
  BLT Detuning method
  Sequential Loop Tuning
  Independent Loop Tuning

## Slide 5
Individual Loop Tuning (McAvoy method)
Sequential Loop Tuning
Tune controller for any one loop (say 1-1 loop when other loops open) and keep 1-1 loop closed
Identify the transfer function of 2-2 loop (with 1-1 loop closed) and Tune the controller for this loop transfer function. Close 2-2 loop
Identify the transfer function of 1-1 loop and tune the controller for 1-1 loop.
Repeat the process till a desired performance achieved.

## Slide 6: Biggest Log Modulus Tuning (BLT)
SISO Loop Design Review:
Characteristic Eqn.
Nyquist Plot: depicts real part of GOL(s) on X-axis and imaginary part of GOL(s) on Y-axis as
Nyquist Stability Criteria:
A feedback control system will be unstable if the Nyquist plot of G(j) encircles point (-1,0) as
The number of encirclements correspond to the number of roots of the characteristic equation that lie in R.H.P. of s –plane assuming that the process is open loop stable.

## Slide 7: BLT Method
A measure of distance of GOL(j) contour from (-1,0) is given as
Suggested design specification for Log Modulus:
Log Modulus Design:
Iteratively choose PI controller parameters such that the design specification is met.
Multivariable Process :
Characteristic Eqn. :

## Slide 8: BLT Method
Define
Encirclement of (-1,0) by f(j) would indicate instability.
Define a multivariable closed loop log modulus as
Suggested design specification for Log Modulus: for n-dimension system
Tuning Procedure
Calculate Ziegler -Nichol's tuning for n individual PI controllers
Assume a factor F such that 2 ≤ F ≤ 5
De - tune PI controllers as follows:
for j=1,2,.. N
Iteratively choose F such that criteria Lcm = 2n is satisfied.

## Slide 9: BLT: Example

## Slide 10: BLT: Example

## Slide 11: BLT: Example

## Slide 12: Dynamic RGA
Process Model:
Dynamic RGA

## Slide 13: Principles of Decoupling

## Slide 14: Block Diagram : Quad Tank

## Slide 15: Simplified Decoupling
Two compensator Blocks gI1 and gI2
Controller output v1 and v2
Actual control on the process u1 and u2
Without compensator
u1 = v1 and u2=v2
Process model :
With Compensator
Loop 2 informed of changes
of v1 by gI2 and u2 is adjusted
Same for Loop 1

## Slide 16: Simplified Decoupler Design
Process Model
u-v relation:
So,
Or,

## Slide 17: Simplified Decoupler Design
Ideally, should be affected by only and should be affected by only. This means,
So,
and

## Slide 18: Simplified Decoupler Design
Decoupler Equation
Steady State Decoupler

## Slide 19: Quad tank : Decoupler Design
Steady State Decoupler :

## Slide 20: Quad tank : Decoupler Design
Full Decoupler :

## Slide 21: Example: Wood Berry Distillation Column

## Slide 22: Difficulties in simplied Decoupler design

## Slide 23: Generalized Decoupler Design

## Slide 24: Example: Wood Berry Distillation Column

## Slide 25: Steady State Decoupler Design

## Slide 26: Example: Wood Berry Distillation Column

## Slide 27: Simplified Vs Generalized Decoupler

## Slide 28: Challenges in Decoupler Design

## Slide 29: Challenges in Decoupler Design

## Slide 30: Example Problem

## Slide 31: Example Problem
Alternate Solution

## Slide 32: Partial Decoupling

## Slide 33: Partial Decoupling Example